| CarType/number: Date: | ( | ( |
| --- | --- | --- |
| Test-drive before start of work |  |  |
| Check new parts relating to assignment/completeness |  |  |
| Measure body-level (wheelcenter to bottom-edge of wing) FL____ FR____ RL____ RR____ |  |  |
| Obey conditions of rim- and suspension-manufacturer |  |  |
| Check vehicle for existing damages |  |  |
| Remove shock absorbers |  |  |
| Check condition of used shock absorbers |  |  |
| Install new components |  |  |
| Check for contact between wheels and body |  |  |
| Check pretension of springs |  |  |
| Measure body-level (wheelcenter to bottom-edge of wing) FL____ FR____ RL____ RR____ |  |  |
| Check geometry of both axles, correct if required |  |  |
| Check adjustment of brake-valve |  |  |
| Check height of headlights |  |  |
| Check headlight beam setting, correct, if required |  |  |
| Check height of number-plate |  |  |
| Check height of trailer coupling, if existing |  |  |
| Test-drive: road behaviour, noise |  |  |
| Let register suspension system, if required |  |  |

*If you only change the shock- absorber, you don`t have to do points: 2. | 3. | 8. | 10. | 12.-16. | 18.

# Text boxes

Guideline for lowering

Shock-absorber change*/Airspring change